## Slide 1
Tutorial : interfacing an HD44780 LCD Display with STM32L4
Jean-Christophe Toussaint Phelma Grenoble-INP
STM32L4 Series
The HD44780 is a widespread common LCD controller allowing to drive various formats
of LCD displays made of 1 line with 8 characters (1X8), 2X16, 2X20, 4x20 or others.
The goal is to show how a GPIO library originally developed for a STM8s MCU (AN4032) can
be easily modified for a STM32 MCU.
The following equipment is used
- NUCLEO-L476RG Board or equivalent and a 2X16 HD44780 LCD display
- Eclipse with the necessary packages for Nucleo boards installed
- OpenOCD or STLink USB Driver - STM32CubeMX

## Slide 2
Generating the config. files from STM32CubeMX.
  Open STM32CubeMX and open a new project.
  Select the Nucleo-L476RG from the Boards tab
  HIS Resonator Clock with PLLCLK is selected by default

## Slide 4
  Go to Project Settings > Generate code
  Enter a project name and select SW4STM32
  Generate the code and open the project in Eclipse IDE

## Slide 5: Example of Application : code to be inserted in main.c
/* USER CODE BEGIN Includes */
#include <stdarg.h>
#include <stdio.h>
#include <HD44780.h>
/* USER CODE END Includes */
/* USER CODE BEGIN PV */
/* Private variables ---------------------------------------------------------*/
/* Exported types ------------------------------------------------------------*/
/* Define 6 custom characters to display bar graph*/
char STCustom[48] =
{
0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, 0x00, // Blank
0x10, 0x10, 0x10, 0x10, 0x10, 0x10, 0x10, 0x10, // 1column |
0x18, 0x18, 0x18, 0x18, 0x18, 0x18, 0x18, 0x18, // 2columns ||
0x1c, 0x1c, 0x1c, 0x1c, 0x1c, 0x1c, 0x1c, 0x1c, // 3columns |||
0x1e, 0x1e, 0x1e, 0x1e, 0x1e, 0x1e, 0x1e, 0x1e, // 4columns ||||
0x1f, 0x1f, 0x1f, 0x1f, 0x1f, 0x1f, 0x1f, 0x1f, // 5columns |||||
};
/* USER CODE END PV */

## Slide 6
/* USER CODE BEGIN 2 */
LCD_INIT();
LCD_CLEAR_DISPLAY();
/* Set @CGRAM address start */
LCD_CMD(CGRAM_address_start);
/* Loading 6 characters @CGRAM address from STCustom tab */
LCD_LOAD_CGRAM(STCustom, 6);
/* Set cursor to the chosen position*/
LCD_LOCATE(1, 1);
/* Print string on LCD (must be ended with \n)*/
LCD_printstring("* STM32-L476RG \1\2\3\4\5 *\n");
/* Print string on LCD (must be ended with \n)*/
LCD_LOCATE(2, 1);
LCD_printstring("* Nucleo Board \1\2\3\4\5 *\n");
/* USER CODE END 2 */
/* USER CODE BEGIN 3 */
LCD_RSHIFT();
HAL_Delay(1000);
}
/* USER CODE END 3 */
LCD_printing allows to
print common characters
and user defined ones.

## Slide 7
Part of the AN4032 application note

## Slide 8
/**
******************************************************************************
* @file HD44780.c
* @author MCD Application Team
* @version V1.0.0
* @date 16_January-2012
* @brief HD44780.c
* originally developed for STM8s
*
* adapted by JC Toussaint Phelma Grenoble-INP for STM32
* @date 18_February-2018
******************************************************************************
* @attention
*
* THE PRESENT FIRMWARE WHICH IS FOR GUIDANCE ONLY AIMS AT PROVIDING CUSTOMERS
* WITH CODING INFORMATION REGARDING THEIR PRODUCTS IN ORDER FOR THEM TO SAVE
* TIME. AS A RESULT, STMICROELECTRONICS SHALL NOT BE HELD LIABLE FOR ANY
* DIRECT, INDIRECT OR CONSEQUENTIAL DAMAGES WITH RESPECT TO ANY CLAIMS ARISING
* FROM THE CONTENT OF SUCH FIRMWARE AND/OR THE USE MADE BY CUSTOMERS OF THE
* CODING INFORMATION CONTAINED HEREIN IN CONNECTION WITH THEIR PRODUCTS.
*
* FOR MORE INFORMATION PLEASE READ CAREFULLY THE LICENSE AGREEMENT FILE
* LOCATED IN THE ROOT DIRECTORY OF THIS FIRMWARE PACKAGE.
*
* <h2><center>&copy; COPYRIGHT 2011 STMicroelectronics</center></h2>
******************************************************************************
*/
HD4470 library for STM32

## Slide 9
/* Includes --------------------------*/
#include "main.h"
#include "stm32l4xx_hal.h"
#include <stdarg.h>
#include <stdio.h>
#include <HD44780.h>
uint16_t GPIO_ReadOutputData (GPIO_TypeDef *GPIOx){
return GPIOx->ODR;
}
void GPIO_Write (GPIO_TypeDef *GPIOx, uint16_t PortVal){
GPIOx->ODR=PortVal;
}
void LCD_CMD(unsigned char cmd_data)
{
HAL_GPIO_WritePin(LCDControlPort, LCD_RS, GPIO_PIN_RESET);
/*
* When the I/O port is programmed as output
* a read access to the output data register gets the last written value.
*/
GPIO_Write(LCDPort, (GPIO_ReadOutputData(LCDPort) & 0xF0) | ((cmd_data >> 4) & 0x0F));
LCD_ENABLE();
GPIO_Write(LCDPort, (GPIO_ReadOutputData(LCDPort) & 0xF0) | (cmd_data & 0x0F));
LCD_ENABLE();
HAL_Delay(2);
}
GPIO_ReadOutputData allows us to read
the GPIOx port value and
GPIO_Write to assign it a value
After that, the translation of the
LCD_CMD function for STM32 is
straightforward
A small part of the library adapted for STM32

## Slide 10: Eclipse Configuration
Parallel building with N (=3 here) processes

## Slide 11
Add ../Drivers/HD44780_Driver to the list of include paths
Include
Paths

## Slide 12
Compile and then
Run as a STM32 runtime

## Slide 13: Wiring

## Slide 14
In Practice

## Slide 15
1. Carmine Noveillo, “Mastering STM32”, https://leanpub.com/mastering-stm32
2. Marc Laury, “A la découverte des cartes Nucleo”, Eyrolles, EAN13 : 9782212673692
3. Reference Manual for STM32L4, DM00083560.pdf
4. Application Note AN4032 , “Interfacing an HD44780 2-line LCD display
with the STM8SVLDISCOVERY ”
References